## Slide 1
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
금일 수행 업무 |  |  |  | 
1 | CI30 | 2P calibration: Simplified calibration logic by removing complex and conflicting state machines. Reworked motor control handling: Ensured proper driver state transition before issuing movement commands. Introduced consistent motor activation logic (handling OFF / STALL conditions). Modified calibration sequence to enforce: Initial movement away from mechanical end Continuous movement toward end-stop until stall detection Reverse direction for full stroke coverage | O | 
이슈 및 리스크 사항 |  |  |  | 
1 | CI30 | Motor behavior became unstable during refactoring: In some cases, motor did not start at all In other cases, calibration triggered but did not complete Calibration inconsistencies: Sometimes detects only one end Sometimes performs partial movement instead of full stroke Command handling issues: Default (CMD 0) intermittently not responding Allow Operation (CMD 1) not functioning due to missing or invalid calibration span System instability introduced due to: Mixing old and new logic during transition phase Incorrect state variable usage and incomplete cleanup of legacy code |  | 
익일 계획 |  |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”

## Slide 2
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
익일 계획 |  |  |  | 
1 | CI30 | Re-establish stable baseline motor movement: Verify motor runs reliably with direct position commands Implement minimal and robust calibration logic: Ensure motor starts reliably Move to first end until confirmed stall Reset position reference Move to opposite end with sustained command Capture full span reliably Ensure: Continuous target updates during movement Proper stall detection validation at both ends Reintroduce functional layers step-by-step: Default positioning (CMD 0) Calibration (CMD 2) Normal operation (CMD 1) Perform controlled testing: Multiple calibration cycles for repeatability | O | 
Summary |  |  |  | 
1 | CI30 | Today’s work focused on simplifying and stabilizing the system after identifying over-complexity and conflicting logic as key issues. While system behavior temporarily degraded during refactoring, critical insights were gained regarding driver interaction and real-time control requirements. The next phase will prioritize rebuilding a stable foundation before reintroducing full functionality. |  | 
1 | CI30 |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”