## Slide 1
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
금일 수행 업무 |  |  |  | 
1 | CI30 | Actuator Calibration & Control Optimization (CI30) Enhanced stall recovery logic Added retry mechanism (up to 3 attempts) Prevented continuous pushing at end stops Attempted integration of runtime 1-point calibration (1P) Triggered after recovery failure Movement to nearest end with overshoot implemented Implemented 1P calibration handler Stall detection + position reset (DRV_ResetPosition) Improved backlash synchronization after stall Added blocking logic during recovery/calibration Prevent RUN mode interference | O | 
이슈 및 리스크 사항 |  |  |  | 
1 | CI30 | After integrating 1P calibration: ❌ Motor stopped responding to LIN commands ❌ System remained stuck in calibration/recovery state Root causes identified: 1P calibration handler blocking main control loop Improper state exit after calibration Incorrect integration with existing mode/state logic Due to instability: 🔄 Recent changes were reverted to last stable version |  | 
익일 계획 |  |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”

## Slide 2
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
익일 계획 |  |  |  | 
1 | CI30 | Re-implement 1-point calibration (1P) in controlled manner Integrate without blocking LIN communication Ensure proper state exit after completion Refactor state handling Clear separation between: RUN RECOVERY CALIBRATION (1P / 2P) Improve stall recovery flow Retry → if fail → controlled 1P calibration trigger Add safety conditions Timeout for calibration Fail-safe fallback to RUN mode Validate: LIN responsiveness during all modes Direction handling and backlash after recovery Perform incremental testing Add one feature at a time (avoid full integration issues) Summary : Core system remains stable and functional Advanced features (1P calibration + enhanced recovery) need careful reintegration Focus shifting from implementation → safe integration & stability | O | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”