## Slide 1
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
금일 수행 업무 |  |  |  | 
1 | CI30 | Actuator Validation : RPM, Torque, Noise • Validated actuator performance based on software implementation • Verified PPS and calculated RPM alignment with requirements • Evaluated torque behavior based on current and speed profile • Improved motion stability using backlash compensation • Verified smooth actuator movement across full range • Validated stall detection and recovery behavior • PPS derived from driver configuration • RPM calculated using step resolution (6400 steps/rev) • Results aligned with requirement range (~2.7–5 RPM) • Hardware validation pending (oscilloscope/physical measurement) • Torque estimated based on motor current and speed • Pull-in torque verified via smooth acceleration | O | 
이슈 및 리스크 사항 |  |  |  | 
1 | CI30 | • Minor positional deviation near end limits (~100 steps) • Torque margin may reduce at high speed / low voltage • Backlash tuning requires further refinement • Default position handling – pending implementation |  | 
익일 계획 |  |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”

## Slide 2
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
익일 계획 |  |  |  | 
1 | CI30 | Perform torque validation under load and voltage variation • Fine-tune backlash and calibration accuracy • Implement and validate default position logic • Conduct full-range robustness testing | O | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”