## Slide 1
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
금일 수행 업무 |  |  |  | 
1 | CI30 | Tested LIN communication between ECU and actuator using CANalyzer. Verified communication of ACTU_01_Req and Act_01_Res frames and confirmed correct signal scaling based on LDF configuration (0–10000 corresponding to 0–100%). Worked extensively on actuator calibration logic (2-point self-calibration) using stall detection: Implemented calibration state machine (GO_END1 → WAIT → REVERSE → DONE) Integrated motor driver functions (DRV_SetTarPosition, ClearStallState, DRV_ResetPosition) Ensured proper driver state transitions (OFF → HOLD → RUN) Debugged actuator behavior during calibration: Observed continuous calibration loop issues Identified incorrect handling of stall state and motor restart Fixed improper target updates causing toggle movement instead of full stroke travel Validated actuator response for: CMD_ALLOW_OP (normal movement) CMD_CALIB (calibration trigger) Analyzed actual position feedback during movement and compared with target position. | O | 
이슈 및 리스크 사항 |  |  |  | 
1 | CI30 | Observed inconsistent actuator behavior during calibration: Motor sometimes performs small movement instead of full stroke Calibration occasionally runs continuously without stopping Direction reversal behaves like toggle instead of controlled sweep Identified root causes: Improper motor driver state transition (HOLD state not entering RUN) Incorrect use of DRV_SetTarPosition() without forcing restart Missing reset sequence before large movements Weak reverse movement after stall detection Additional risks: Calibration span not always captured correctly Position mapping may be inaccurate without proper end-stop detection LIN command timing may interfere with calibration flow |  | 
익일 계획 |  |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”

## Slide 2
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
금일 수행 업무 |  |  |  | 
1 | CI30 |  | O | 
이슈 및 리스크 사항 |  |  |  | 
1 | CI30 |  |  | 
익일 계획 |  |  |  | 
1 | CI30 | Finalize and validate stable 2-point calibration logic Ensure actuator covers full stroke (end-to-end) reliably Verify stall detection consistency at both ends Store and validate calibration span (min/max positions) Perform detailed testing: Validate actuator movement across full range (0–100%) Check position mapping accuracy after calibration Test repeatability of calibration over multiple cycles Further improvements: Optimize driver state handling (OFF → HOLD → RUN transition) Improve robustness against incorrect LIN command sequences Ensure smooth transition between calibration mode and normal operation |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”