## Slide 1
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
금일 수행 업무 |  |  |  | 
1 | CI30 | 2P Calibration – Stability & Control Integration Analyzed inconsistency between power-on calibration and CAN-triggered calibration behavior. Identified that calibration instability was not due to core state machine logic, but due to external command interference and driver state conditions during runtime. Refined control architecture by ensuring single control ownership during calibration (blocking external LIN/CAN movement commands while calibration is active). Simplified calibration flow by removing redundant states and excessive retry/handling logic, restoring a deterministic sequence (END1 → BACKOFF → END2). Investigated reverse movement issue after stall and confirmed dependency on driver state (energized vs relaxed condition) rather than logic error. Implemented controlled entry condition for calibration to align CAN-triggered behavior with power-on conditions. Performed multiple validation runs comparing: Power-on calibration vs CAN-triggered calibration CW vs CCW starting positions Current Observation Power-on calibration: stable and repeatable CAN-triggered calibration: forward movement correct, reverse still shows resistance/unstable behavior Target mode functionality partially affected due to control path conflicts (under verification) | O | 
이슈 및 리스크 사항 |  |  |  | 
1 | CI30 | Reverse movement instability persists under LIN-triggered calibration Need further validation of driver ON/OFF timing and load release behavior Potential dependency on motor current / hardware tuning. |  | 
익일 계획 |  |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”

## Slide 2
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
익일 계획 |  |  |  | 
1 | CI30 | Add minimal debug checkpoints for: command issuance driver state before/after movement Verify clean motor state before reverse (post-stall release timing) Fine-tune backoff and reverse sequence without adding state complexity Validate target mode after calibration stabilization | O | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”