## Slide 1
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
금일 수행 업무 |  |  |  | 
1 | CI30 | Actuator Movement Logic – Runtime Protection & Recovery Stabilization Analyzed issues in stepper motor runtime behavior during normal operation, especially under mid-obstacle conditions. Identified root causes of excessive motor force, delayed stall detection, and oscillation between target and mechanical ends. Investigated limitations of relying solely on driver stall status and introduced motion-based detection for early blockage identification. Debugged interaction between movement commands and recovery logic leading to unintended retries and unstable behavior. Refined control flow to ensure proper separation between normal operation, recovery handling, and fail-safe conditions. Verified correct behavior of: Target-based movement using calibrated span (0–10000 mapping) Direction handling based on current actuator position Stable execution under normal (no obstacle) conditions | O | 
이슈 및 리스크 사항 |  |  |  | 
1 | CI30 | Stall detection still partially dependent on driver feedback (RUN / HOLD / STALL), which may introduce delays under certain load conditions No-motion threshold (timing and sensitivity) may require further tuning based on mechanical variations Retry strategy may need refinement for different obstacle types (soft vs hard blockage) Edge cases such as rapid target updates during recovery require additional validation |  | 
익일 계획 |  |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”

## Slide 2
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
익일 계획 |  |  |  | 
1 | CI30 | Perform validation across all operating modes: Default mode (0) Target control mode (1) Calibration mode (2) Test actuator behavior under: Mid-position obstruction scenarios Repeated target updates during recovery Continuous LIN command conditions Fine-tune: No-motion detection threshold Backoff distance and retry timing Improve recovery strategy for smoother behavior (reduce force during retry) Prepare code cleanup and documentation for: Movement logic Recovery state handling Integration with calibration flow | O | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”