## Slide 1
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
금일 수행 업무 |  |  |  | 
1 | CI30 | Actuator Calibration & Control Optimization (CI30) Verified Mode 1 (target-based movement) and Mode 2 (calibration) functionality Implemented and stabilized Default Mode (Mode 0) → Achieved correct positioning to mid target (5000) → Ensured isolation from RUN logic Improved stall detection and recovery logic → Implemented backoff and retry mechanism → Added safe-end handling after multiple retries Fixed position reference handling after stall recovery → Maintained correct span without resetting position Corrected backlash compensation logic → Ensured backlash is applied after recovery → Fixed direction tracking and compensation sequence Optimized motor control flow → Applied backlash before target check → Eliminated dead-zone condition near target Verified stable movement after stall recovery → No abnormal jump or span deviation observed | O | 
이슈 및 리스크 사항 |  |  |  | 
1 | CI30 | Measured RPM 5.07 still exceeds specification upper limit (~5.0 RPM) → Non-compliance risk RPM validation currently based on software timing (no external measurement tool yet) Torque validation not yet performed → Pull-in / Pull-out torque compliance still unknown Residual click noise during calibration reversal (improved but not eliminated) Trade-off observed: Lower speed → better noise Higher speed → RPM compliance risk Calibration depends on stall detection → mechanical variability risk |  | 
익일 계획 |  |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”

## Slide 2
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
익일 계획 |  |  |  | 
1 | CI30 | Fine-tune motion profile to achieve RPM ≤ 5.0 within specification limits Improve backlash compensation behavior → Optimize response during direction change → Ensure stable performance near target positions Enhance stall detection and recovery robustness → Validate performance under different load and voltage conditions → Improve consistency of recovery behavior Transition toward state-machine-based control architecture → Align current logic with reference implementation for better stability Improve calibration stability and repeatability → Ensure consistent span calculation across cycles Optimize noise performance during direction reversal and end-stop approach Validate mode transition behavior (Default / Run / Calibration) → Verify position accuracy and retention → Check behavior after stall, reset, and power cycles Perform LIN communication and diagnostic validation → Cover RPM, torque, calibration stability, and long-run reliability | O | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”