## Slide 1
Design Proposal for 5.5kW HV PTC Heater
WOORY
“ 생각을 바꾸고 연구소를 다시 만든다 ”

## Slide 2
PTC Heater Electric Generals
Zone 1
Zone 2
Two Zone :
- PTC Heater Performance : 5.5kW ±5%
- HV & LV circuits are in One PCB Board
Ingress Protection : IP67
Heating Rod type : Aluminum tube type
Fin Type : Brazing Fin (Separated type)
Connector Type : Direct Connector HV, LV (IP67)
- HV Connector : APTIV 35415839
→ Mating Connector : APTIV 35415834
- LV Connector : KET MG651098-5
→ Mating Connector : KET MG641101-5
Chassis GND is necessary to meet the EMC spec.

## Slide 3
PTC Heater Dual Zone Concept
175
78
40
269
134
32
No | Item | Unit | Spec | Remark
1 | Size(L x H x T) | mm | 269 x 134 x 32 | Core part
 |  |  | 175 x 78 X 40 | Control part
2 | Power (0℃, 300kg/h, 357V) | kW | 5.5 ±5% | -
3 | Steady Current | A | 15.4A ±5% | @Nominal condition
4 | Inrush Current | A | Max. 20A | -
5 | Pressure Drop | Pa | MAX 115Pa | -
6 | Normal Voltage | Vdc | 358 | -
7 | HV Range | Vdc | 150~432V | -
8 | LV Range | Vdc | 8 ~ 18 | -
9 | Communication | - | High Speed CAN | -
11 | Operating Temperature | ℃ | -40 to 85 | -
12 | Storage Temperature | ℃ | -40 to 105 | -
13 | IP Rate | - | IP 67 | -
General Specification

## Slide 4
PTC Heater Dual Zone
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
20
21
22
23
19
19-1
19-2
19-3
19-4
19-5
19-6
No |  | Item | Q’ty | Remark
1 |  | NAME PLATE | 1 | 
2 |  | WARNING LABEL | 1 | 
3 |  | COVER | 1 | 
4 |  | VENT FILTER | 1 | 
5 |  | MAIN PCB ASS’Y | 1 | 
6 |  | CHASSIS GROUND WIRE ASS’Y | 1 | 
7 |  | HV CONNECTOR ASSY | 1 | 
8 |  | SIGNAL CONNECTOR ASS’Y | 1 | 
9 |  | JOIN BOARD ASS’Y | 1 | 
10 |  | SEALANT | 1 | 
11 |  | IGBT PAD | 1 | 
12 |  | IGBT | 3 | 
13 |  | UPPER HOUSING ASS’Y | 1 | 
14 |  | SIDE BAR | 2 | 
15 |  | LOWER HOUSING | 1 | 
16 |  | HEAT CORE ASS’Y | 1 | 
17 |  | BRAZING FIN - A | 11 | 
18 |  | BRAZING FIN - B | 3 | 
19 |  | HEAT ROD ASS’Y | 6 | 
 | 1 | AL TUBE | 1 | 
 | 2 | INSULATION PAD | 2 | 
 | 3 | TERMINAL UPPER | 2 | 
 | 4 | PTC STONE | 8 | 
 | 5 | STONE HOLDER | 1 | 
 | 6 | TERMINAL LOWER | 2 | 
20 |  | UPPER GROMMET | 1 | 
21 |  | SPONGE | 1 | 
22 |  | CORE JOIN FIXTURE | 1 | 
23 |  | TEMPSENSOR FIXTURE | 2 | 
비고 |  |  |  | 
■ Exploded View
■ Part List

## Slide 5
HV & LV Connector information
Connector | Part number | Pin No. | Pin name | Remark
HV Connector | APTIV 35415839 (Mating : Aptiv 35415834) | 1 | HV(+) | 
 |  | 2 | HV(-) | 
 |  | 3 | Interlock(+) – HV PTC | 
 |  | 4 | Interlock(-) – HV PTC | 
LV Connector | KET MG 651098-5 (Mating : KET MG 641101-5) | 1 | IGN3 | 
 |  | 2 | CAN HIGH | 
 |  | 3 | CAN LOW | 
 |  | 4 | GND | 
■ Connectors & Pin map

## Slide 6
IP Waterproof structure
SIGNAL CONNECTOR
HV
CONNECTOR
MEMBRANE
FILTER
HEAT ROD
COVER
HEAT ROD |  |  | 
HV CONNECTOR |  | LV CONNECTOR | 
COVER |  |  | 
A
A
SECTION VIEW A-A
실리콘 충진 부
Silicon Filling Area
SECTION VIEW B-B
LOWER HOUSING
ROD ASS’Y
A
UPPER HOUSING
HEAT ROD
GROMMET
B
B
SECTION VIEW C-C
HV GROMMET
UPPER HOUSING
C
C
SECTION VIEW D-D
LV GROMMET
UPPER HOUSING
D
D
SECTION VIEW E-E

## Slide 7
Mounting Direction & air flow direction
HVAC MT’G Direction
AIR FLOW
AIR FLOW

## Slide 8
BLOCK DIAGRAM
Block diagram
HV(+)
IGN(+)
HV(-)
HV circuit
LV circuit
GND(-)
Core FIN
Core FIN
Core Ass’y
Interlock
Isolation
IGBT1
Core FIN
Core FIN
CAN_ L
Current Sensing1
Shunt2
Shunt1
CAN_ H
PCB Temp Sensor
IGBT2
LC Filter
Current Sensing2
High Voltage Sensing
IGBT3
A
T
C
U
DC/DC
Switching IC
Regulator
LV Sensing
Chassis GND
CAN
Transceiver
Connector
Connector
Transformer
Connector
Digital
Isolator
TXD
RXD
Sidebar Temp Sensor1
Sidebar Temp Sensor2
MCU
Interlock
Gate Driver
Gate Driver
Gate Driver
Regulator
ELEC - CAPCITOR

## Slide 9
Protect Functions
NO | ITEM | Specification | Logic | Functions
1 | LV under Voltage | LV Voltage ≤ 8V (Hysteresis 1.0V) |  | protecting over discharging of the LV Batt Protecting abnormal operating in the under voltage condition of LV
2 | LV Over Voltage | LV Voltage ≥ 17V (Hysteresis 1.0V) |  | Protecting abnormal operating in the over voltage condition of LV
3 | HV under Voltage | HV Voltage ≤ 150V (Hysteresis 20V) |  | Protecting rapid discharging of the HV Battery Protecting abnormal operating in the under voltage condition of HV
4 | HV Over Voltage | HV Voltage ≥ 432V (Hysteresis 20V) |  | Protecting abnormal operating in the over voltage condition of HV
5 | HV Over Current | HV Over Current ≥ TBD |  | Do not exceed 14A by controlling the performance by itself. (Each Zone) Protecting PTC heater from over current conditions (Each Zone)
6 | PCB Over Temp | PCB Temp ≥ 105℃ (Hysteresis 10℃) |  | Protecting PTC heater circuits from its heat.
7 | Core Over Temp | Core Temp ≤ 95℃ Core Temp ≥ 105℃ (Hysteresis 10℃) |  | Protecting PTC heater circuits from its heat. Reduces performance according to overheating temperature
17V (TBD)
18V (TBD)
STOP
RUN
170V (TBD)
150V (TBD)
STOP
RUN
412V (TBD)
432V (TBD)
STOP
RUN
95℃
105℃
STOP
RUN
14A (TBD)
STOP
RUN
9V (TBD)
8V (TBD)
STOP
RUN
after 10sec
95℃ (TBD)
105℃(TBD)
STOP
RUN

## Slide 10
No | Function | Description | Remark
1 | Power Control | - Pulse Width Modulation (6Hz) - The period is kept constant while the ON time (pulse width, duty cycle) is adjusted. | 
2 | Consumption Power Control | Power Mode : Linear power control according to watt command Max Stable Current Control Max Inrush Current Control | 
3 | Communication | LIN Communication | 
4 | Monitoring | LV, HV Voltage Monitoring HV Current monitoring Consumption Power Monitoring PCB & core temp sensor temperature monitoring | Need to define within LIN Spec Data List
5 | Protection Function | - LV Out of Range fault (Under / Over Voltage) - HV Under / Over Voltage fault - HV Over Current fault PCB / Over Temperature fault Temp Sensors (Core part) / Over Temperature fault Communication Error fault control | See next page
6 | Failure Detection | Sensor Failures (HV, HV Current, Temp Sensors) IGBT Short failure | See next page
Product Specifications
■ Product Specifications Review : Introduction to Key Features

## Slide 11
◎ Failure List
ITEM | DETAIL | NOTE
CoreTempSensor | Core temperature sensor failure | 
HighVoltSensor | High voltage sensor | 
LowVoltSensor | Low voltage sensor | 
PcbTempSensor | PCB temperature sensor | 
IGBT | IGBT failure in eachr zone | 
OverCurrent | Over Current failure | 
HVHigh | Over voltage failure in high voltage | 
HVLow | Low voltage failure in high voltage | 
LVHigh | Over voltage failure in low voltage | 
LVLow | Low voltage failure in low voltage | 
PcbOverTemp | PCB temperature overheating failure | 
CoreOverTemp | Core temperature overheating failure | 
CAN Communication Timeout | CAN communication timeout failure | 
InterLock | Interlock not inserted failure | 
◎ OPERATION FeedBack List
ITEM | DETAIL | NOTE
IGBT Operating Frequency Duty (%) | Feedback on ther current frequency applied to IGBT | 
Operating Power (%) | Feedback on the current power as a percentage | 
Operating Power (W) | Feedback on the current power | 
Operating Current (A) | Feedback on the current current | 
LIN Communication List

## Slide 12
NO | Item | Description
1 | ISO 26262 Status | - ASIL B achieved in another project
Question |  | 
1 | ISO-21434 (Cyber Security) | - Cyber Security is applied (Y/N)
2 | A-SPICE | - A-SPICE is appliedis applied (Y/N)
Other Information