## Slide 1
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
금일 수행 업무 |  |  |  | 
1 | CI30 | 2P Calibration: Performed detailed analysis of motor driver (motor_driver.c) behavior. Confirmed: Direction reversal is only applied during HOLD → RUN transition. Target updates during RUN do not ensure reversal. Implemented controlled reversal logic using: Driver reset (OFF → ON) Explicit direction setting (CW / CCW) Improved calibration sequence: Removed continuous target updates Added controlled state-based motion Integrated stall detection handling Current Behavior (New Observation): After reaching second end (End B): Motor attempts reversal multiple times (3–4 attempts). Moves back toward first end (End A). Then again reverses direction. This cycle repeats continuously. | O | 
이슈 및 리스크 사항 |  |  |  | 
1 | CI30 | Calibration not fully stable yet. Motor reaches first end (End A) correctly. Reverse movement: Infinite calibration Sometimes delayed or not initiated. Occasionally depends on starting position. Observed oscillation near end regions in some cases. |  | 
익일 계획 |  |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”

## Slide 2
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
익일 계획 |  |  |  | 
1 | CI30 | Stabilize reversal logic completely: Enforce HOLD → direction set → RUN sequence Ensure motor exits stopper region before reverse detection Validate full calibration sequence: Move to End A (stall) Clear stall + enter HOLD Reverse direction Move to End B Capture full span Improve robustness: Add retry mechanism (max 2–3 attempts) Add timeout handling Handle edge cases: Start at End A Start at End B Near-end starting position Mid-range starting position Eliminate oscillation completely After stabilization: Enable Default operation (CMD 0) Enable Allow operation (CMD 1) only after successful calibration | O | 
Summary |  |  |  | 
1 | CI30 | The system now correctly detects both end positions; however, calibration does not terminate properly. After reaching the second end, the motor repeatedly attempts to reverse direction, causing continuous oscillation between end positions. This confirms that while direction control and stall detection are functioning, the calibration state machine lacks a proper termination condition and lock mechanism. Next steps focus on enforcing a strict end-of-calibration stop condition to achieve stable and repeatable 2-point calibration. |  | 
1 | CI30 |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”