## Slide 1
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
금일 수행 업무 |  |  |  | 
1 | CI30 | 2P Calibration – Integration stabilization for Auto and CAN-triggered calibration Analyzed integration issues between power-on auto calibration and CAN command-based calibration. Identified root cause of continuous oscillation due to repeated CALIB command triggering from CANalyzer. Investigated driver state dependencies (RUN / HOLD / STALL) affecting calibration start conditions. Debugged conflicts between normal operation modes and calibration state machine execution. Verified correct execution of: Power-on auto calibration sequence CAN-triggered calibration sequence Implemented key fixes: Ensured motor enters HOLD state before starting calibration Prevented calibration restart during continuous CAN command frames Introduced edge-trigger handling for CALIB command to avoid repeated execution Stabilized interaction between LIN command handling and calibration logic Current Observation: Calibration is now functioning correctly and consistently for both power-on and CAN-triggered scenarios. Continuous oscillation issue has been resolved. Calibration sequence executes reliably with proper end-stop detection and direction reversal. | O | 
이슈 및 리스크 사항 |  |  |  | 
1 | CI30 | Calibration still depends on correct synchronization with driver states (RUN / HOLD / STALL). Stability relies on proper command handling; incorrect or noisy LIN signals may still affect behavior. Edge cases such as: Mid-position start Rapid mode switching (0 / 1 / 2) may require further validation. Stall detection sensitivity and settling timing may need fine-tuning for different mechanical conditions. |  | 
익일 계획 |  |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”

## Slide 2
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
익일 계획 |  |  |  | 
1 | CI30 | Perform full validation across all operating modes: Default mode (0) Target control mode (1) Calibration mode (2) Test calibration robustness under different initial positions and repeated command scenarios. Fine-tune stall detection thresholds and settling delays for improved reliability. Validate behavior under continuous CAN/LIN communication load. Prepare final code cleanup and documentation for calibration logic and integration flow. | O | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”