## Slide 1
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
금일 수행 업무 |  |  |  | 
1 | CI30 | 2P Calibration: Attempted to integrate immediate back‑off logic after stall detection in calibration routine. Modified CAL_FIND_END1 and CAL_FIND_END2 states to send retreat commands directly after stall. Tested calibration sequence with new changes. Observed that motor did not respond after modification → driver commands not executed as expected. Conducted debugging: checked move_sent flag handling, stall clear logic, and driver state transitions. Identified that termination condition may be blocking motion prematurely. Current Behavior (New Observation): Motor fails to move after applying new calibration changes. No progress in calibration sequence; driver remains idle. Indicates possible logic error in state machine (command not issued or state stuck). | O | 
이슈 및 리스크 사항 |  |  |  | 
1 | CI30 | Calibration not functional with current changes. Risk of further delay if stall/back‑off handling is not corrected. Need to confirm driver ON/OFF transitions and command issuance. . |  | 
익일 계획 |  |  |  | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”

## Slide 2
항목 | 주요내용 | 조치내용 | 완료 여부 | 비고
익일 계획 |  |  |  | 
1 | CI30 | Add debug logging for state transitions and target positions. Verify driver status before and after each DRV_SetTarPosition(). Re‑test with minimal back‑and‑forth move routine to confirm motor driver functionality. Refine calibration state machine to ensure commands are sent and executed. | O | 
Vignesh
“ 생각을 바꾸고 연구소를 다시 만든다 ”